## Slide 1: Color Wheel
Color science

## Slide 11: RGB vs. HSV

## Slide 12: RGB
For the purposes of this survey, we’re working inside the RGB space of the average monitor, so this data is useful for picking and naming screen colors. And really, if you’re reading this blog, odds are you probably—like me—spend more time looking at a monitor than at the outdoors anyway.
- https://blog.xkcd.com/2010/05/03/color-survey-results/

## Slide 13: HSV = HSB / HSL
Advantage over RGB: more intuitive way of finding colors
HSV = hue, saturation, value
HSL = hue, saturation, lightness
Hue (color):
  Color wheel color
  Domain = [0, 360°] in degree angles
  To categorize into intervals of basic colors
Saturation:
  Domain = [0, 100] in percent, where 0 is gray and 100 is the pure color
  Adding gray desaturates (achromatic = colorless), removing gray saturates (=chromatic)
  To «tone» the color
Value/brightness:
  Domain = [0, 100] in percent, where 0 is black and 100 is the pure color
  Adding black darkens, removing black lightens
  To «shade» the color
Lumination:
  Doamin =[0, 100], where 0 is black, 50 is the pure color (=value) and 100 is white
  Adding black darkens, adding white lightens
  To «shade» and to «tint» the color
Pure hue has no white, black, gray or complementary color in it.
Hue Specification:
Red falls between 0 and 60 degrees.
Yellow falls between 61 and 120 degrees.
Green falls between 121-180 degrees.
Cyan falls between 181-240 degrees.
Blue falls between 241-300 degrees.
Magenta falls between 301-360 degrees.
https://www.lifewire.com/what-is-hsv-in-design-1078068

## Slide 14: HSV color wheel in 30°-steps on hue wheel

## Slide 15
0°
180°
90°
270°
30°
60°
120°
150°
210°
240°
300°
330°
red
orange
yellow
Green-yellow
Green
Green-blue
cyan
Blue-yellow
blue
purple
magenta
Red-yellow

## Slide 16: HSV Color Wheel: Center + Range detection
8 color categories
Tweaked based on looking at HSV color wheel colors
Red: 0°; range: ]337.5°-15°]
Orange: 30°; range: ] 15°-45°]
Yellow: 60°; range: ] 45°-60°]
Green: 120°; range: ] 60°-150°]
Cyan: 180°; range: ] 150°-202.5°]
Blue: 225°; range: ] 202.5°-247.5°]
Violet: 270°; range: ] 247.5°-292.5°]
Magenta: 315°; range: ] 292.5°-337.5°]
https://www.lifewire.com/what-is-hsv-in-design-1078068

## Slide 17: HSV Color Wheel: Center + Range detection
8 color categories
Tweaked based on looking at color visualization of HSVs and http://hslpicker.com at border points
Cyan- and – green border is very hard to determine by waterfall color plotting
Manual tweaking:
{'red': {'pure': 355, 'range': [341,10]}
, 'orange': {'pure': 25, 'range': [11,40]}
, 'yellow': {'pure': 50, 'range': [41,60]}
, 'green': {'pure': 115, 'range': [61,170]}
, 'cyan': {'pure': 185, 'range': [171,200]}
, 'blue': {'pure': 230, 'range': [201,260]}
, 'violet': {'pure': 275, 'range': [261,290]}
, 'magenta': {'pure': 315, 'range': [291,340]}
}

## Slide 18: LCH(ab) Color Wheel: Center + Range detection
1. Visual inspection of image to the left:
Constant chroma: 100
Luminance + hue: variations
An approximation:
{'red': {'pure': [50, 100, 20]}
, 'orange': {'pure': [70, 100, 30]}
, 'yellow': {'pure': [90, 100, 50]}
, 'green': {'pure': [50, 100, 70]}
, 'cyan': {'pure': [100, 100, 300]}
, 'blue': {'pure': [30, 100, 310]}
, 'violet': {'pure': [0, 100, 320]}
, 'magenta': {'pure': [70,100,360]}
}
2. Convert color category centers directly from the HSV table.

## Slide 19: Color Wheel: Range detection
+ 3 non-colors:
Black, gray and white
Black is defined as an interval in value
Value = [0, 20]
Gray is a function with saturation and value as parameters.
Determine gray with regression and plotting some hsv points in 2D.
Linear function best suited among all other functions, because highest R2 for 10 data points.
Saturation = [0, sat] where: Value = -0.75 sat + 95 and sat = [0,100] and value = [20,95]
White is defined with saturation and value as parameters
Saturation = [0, sat], where sat = value – 95 and value = [95, 100)

## Slide 21
Wrong HSV color wheel found on google:
Dotter and violet colors are not on any 30° multiple of the wheel
Blue-yellow color is missing on the color wheel

## Slide 22: HSV color wheel
Disadvantage
The color wheel has green and blue areas that are relatively big as compared to yellow, but where no qualitative differences in hue are perceptible – the greens and blues stay the same
Solution: use LAB (=RGB) and LCH (=HSV) color space to have steps where colors are perceptually equally distant to the human eye
The greens in the seq of colors are not perceptually as different as the reds, for example

## Slide 23: Conversion LAB to LCH
Trigonometry
Use trigonometry to write own conversion function

## Slide 24: L*a*b color wheel
Disadvantage
Now, the colors are perceptually queall distant to the human eye
But, there are three blues, no yellow and three green color categories
Solution: do a linear combination with luminance
No - Solution: get color thesaurus for each of the 12 hues and work out their l*a*b values (see Lindner) – does not work, because ‘red’ is not RGB(255,0,0) due to cultural color naming differences
Basic Colors, Itten p. 22
6 colors: https://colorthesaurus.epfl.ch/
Red, orange, yellow, green, blue, violet
Conclusion: try to break down 12 hues into 6 that fit into these color categories.
Compute borders between hue centers
Problem: no gray, white, black, brown categories

## Slide 25: Color Categories
Disadvantage
Problem: no gray, white, black, brown categories
Solution: Robert M. Boynton. Eleven Colors That Are Almost Never Confused. In SPIE Proc. #1077 - Human Vision, Visual Processing, and Digital Display, pages 322-332, Bellingham, WA, 1989. SPIE.
Not more than 12 color categories
Boynton’s colors: orange, brown, gray, pink, magenta, yellow, green, red, blue, white, black

## Slide 26: Basic Color Categories
For Color Classification

## Slide 27
https://www.w3.org/wiki/CSS/Properties/color/keywords
Basic Colors, Itten p. 22
6 colors: https://colorthesaurus.epfl.ch/
Red, orange, yellow, green, blue, violet
16 colors

## Slide 28
Basic Colors, Itten p. 16

## Slide 29: Color Thesaurus

## Slide 30
Lindner
https://colorthesaurus.epfl.ch/

## Slide 31
Dimitris Mylonas
https://colornaming.net/#colour-namer

## Slide 32: Make a Color Palette
https://medialab.github.io/iwanthue/

## Slide 33: An Optimum 16 CPs
http://alumni.media.mit.edu/~wad/color/palette.html